## Slide 2: Lecture 15: Introduction to Interactive Petrophysics (IP Software)
Principle of IP Software
Working with single well
Introduction to IP:
Navigate IP interface
IP Database
Overview of IP basic workflow

## Slide 3
Introduction to IP:
Loading Log Data
Edit/View Log
Crossplot and Histogram
Introduction to Log plot
Calculation, Env. Corrections

## Slide 4
Application of IP software (Log Interpretation):
Clay Volume Calculation.
Porosity and Water saturation.
Cutoff and Summation.
Exporting well data.
Multi well interpretation

## Slide 5
Principle of IP Software
Interactive Petrophysics is a PC based software application.
Multi well multi zone reservoir property analysis.
Wide range of options
Provide Freedom to explore a range of interpretation before saving to the data base.

## Slide 6: Working with single well
Introduction to IP
Navigate IP interface
IP Database
Overview of IP basic workflow
Data loading
Introduction to log Plot
Log Editing
Cross Plot and histogram

## Slide 7: IP Database
An IP database (project) consists of a group of wells
In set of binary files grouped together in 1 folder
A project holds 9999 wells, with 200 wells loaded onto the memory at one time
Locking Mechanism (IPDB Lock)

## Slide 8: IP Database is
A subdirectory for each IP user using a database
Each well stored in the IP project directory consists of :
  Curve data : IPDBWellxxxx.dat
  General well information : IPDBProj.dat
  Interpretation Parameter : .set(cutoff.set,phisw.set)
  Clay vol. set
  IPD Block file

## Slide 9
Memory well number
-1 means well is not saved in DB.

## Slide 10: Curve Sets
Short name : max of 4 letters and is always appended to the front of the curve name (example, R1:GR)
Long name, used to document the purpose of the set
Notes: In each curve set, the curve name is unique. Curve names can be the same but have to be stored in different curve sets.

## Slide 11: Default File Locations
Input Storage Location
Output Storage Location
Formula Storage Location

## Slide 12: Basic Workflow
Load data
Define log cutoffs
Generate a summary report
View/Edit data
Depth Match, Splice, Env. Corr.
Calculate Volume of Shale
Create zones
Calculate Porosity
Calculate Saturation

## Slide 13: Loading Log Data
Notes: The exercises using the current IP manual will only include ASCII and LAS load.

## Slide 14: Edit/View Log data
Notes: Only the highlighted options will be included in the exercises using current IP manual.

## Slide 15: Log Plot & Data Editing
Similar to Well Composite or Well Edit modules in GeoFrame
Provides a graphical interface to display digital log data
Provides several templates *.plt (like LGP in GeoFrame)
Log Editing
Curve splicing
Depth shifting
SP Baseline
Curve editing
Temp Gradient
Curve Filter and Average
Notes: Demonstration is a must before students do the exercises.
Show the students on how to work with Log Plot.

## Slide 16: Cross Plot Used to analyze relationships between data
Provides statistical regression line-fitting
Provides pre-defined overlays
Users can create areas and generate curves from the areas

## Slide 17: Neutron- Density Cross Plots
This crossplot has b plotted against the corrected neutron porosity
Fluid density in this plot is 1.0 g/cm3

## Slide 19: Calculation, Env. Corrections

## Slide 20: Log Interpretation

## Slide 21: Clay Volume
Single Clay Indicator
Double Clay Indicator
Only single clay indicator
Provide access to Xplot

## Slide 22
Shale line Indicator
Double Clay Indicator
RHOB/NPHI XPlot

## Slide 23: Porosity and Water Saturation

## Slide 24
Reservoir Summation