## Slide 1
Special Topics: Microprocessor & Assembly Language
Instructor: Ghazwan Abdulnabi Al-Ali
University of Basrah, Iraq
2rd Grade
Computer Science Dept/ College of Education for Pure Sciences

## Slide 2: General Architecture of Microcomputer system
The hardware of Microcomputer system can be divided into four functional units:
  Input Unit
  Microprocessing Unit (MPU)
  Memory Unit
  Output Unit

## Slide 3: Memory Unit
Internal Memory.
    used for storage to active information and programs (program to be executed and data under processing).
    ROM & RAM.
  External memory
    used for storage of non active data (long storage).
    CD & Disk drives

## Slide 4: Microprocessor
EU (Execution Unit)
  (EU) Execution unit that responsible of executing instructions ..
  Registers
    Small and fast memory that contains the data that is under process
  ALU (Arithmetic and Logical Unit)
    Executing arithmetic and logical instructions
    And, OR, XOR, NOT
  CU (Control Unit)

## Slide 5: Microprocessor
BIU (Bus Interface Unit)
  BIU controls on Buses and transfers data between EU and memory and External I/0 devices.
  Segment Register
  Segment registers are used to control memory addressing.
  2. Instruction Point
  It is a register to indicate the next instruction to be executed
  3. Instruction Queue
  Note// EU and BIU is parallel, but BIU keeps one step forward (when EU executes an instruction BIU brings another instruction from memory and put it in instruction queue).

## Slide 6: Memory address space and data organization
is organized as bytes of data stored at consecutive addresses from 00000h to FFFFFh ,
these bytes can be independently accessed.
the lower address byte is called the least significant byte and the higher address byte is called the most significant byte.

## Slide 7
8 4 2 1
* * * *
1 1 1 1
8+4+2+1=15=F
8 4 2 1
0 1 1 0
0+4+2+0=6

## Slide 8: Registers
Segment Registers
  CS
  DS
  SS
  ES
Data Registers
  AX
  BX
  CX
  DX
Indexing Registers
  SI
  BP
Point Registers
  SP
  BP
  IP

## Slide 9
Thank You