## Slide 1
Special Topics: Microprocessor & Assembly Language
Lecture 8
Instructor: Ghazwan Abdulnabi Al-Ali
University of Basrah, Iraq
2rd Grade
Computer Science Dept/ College of Education for Pure Sciences

## Slide 2: Generating a Memory Address
Logical address in 8088 described by segment and offset, both segment and offset are 16 bit in length (why) because all registers are 16 bit in length.
Physical address is 20 bit in length ,the generation of physical address involves combining offset value with base(segment) value after shifting it one step to the left.
Logical Address
Segment Offset

## Slide 3: EX:
Find physical address, if segment= 1224h and offset =0032h

## Slide 4: Solution: physical address
Find physical address, if segment= 1224h and offset =0032h
Segment =1224h 12240h
12240h
0032+
______
12272h physical address
Shift left*10

## Slide 5: Ex2:
Find offset when PA=003B3h and Segment=0039h
  PA=Segment*10+offset.
  003B3=0039*10+offset
  Offset=003B3-00390
  =00033

## Slide 6: Addressing modes of 8088
When 8088 executes an instruction, it performs a specified operation on data, these data are called operands, and they may reside in one of the internal registers or stored in memory location or (I/0) port.
To access these different types of operands the 8088 is provided with various addressing modes? and they are.
  Register Addressing Mode
    The operands to be accessed are reside in one of the internal registers such as: MOV AX, BX MOV DH, CL
  Immediate Addressing Mode
    The source is a constant data (byte or word) for example:
    MOV AL, 22 h
    MOV BX, 3324 h

## Slide 7: Addressing modes of 8088 Cont.
  Direct Addressing Mode
    In This type the instruction holds an effective address (EA) instead of data.
    EA is 16 bit offset from the location specified by the value of DS register; this address is combined with the contents of DS to produce the physical address (PA) of the operand in memory for example:
    MOV CX, Alpha effective address EA (Alpha) =l234h and DS=0200
    PA=02000 + 1234h=03234h is the physical address of alpha that contain the data that will be stored in CX.

## Slide 8: Addressing modes of 8088 Cont.
  Register Indirect Addressing Mode
      In this type EA is reside in one of the following registers SI, DI, BX or BP such as:
      MOV AX, [SI] SI=0100 and DS=0300
      PA= DS*10 + EA
      PA=03000+0100=0300 is the physical address of the data that will be stored in AX.
    Based Addressing Mode
      One operands is a base register (BX or BP) with a displacement for example: MOV [BX] + Alpha, AL
      EA= BX+ Alpha, PA= DS*10 + EA
      MOV CH, [BP] + Alpha
      PA=SS*10 + EA where EA=BP + Alpha
    Indexed Addressing Mode
      One operand is an index register (SI or DI) with indirect displacement
      such as: MOV BL, [SI] + Alpha where Alpha is a displacement ,PA=DS*10 +SI+ Alpha

## Slide 9: Addressing modes of 8088 Cont.
    Based Indexed Addressing Mode
      This type combine based addressing with index addressing, i.e. One operands contain base register and index register with displacement such as:
      MOV AH, [BX][SI] + Beta
      EA=BX + SI + Beta
      PA=DS*10 + EA

## Slide 10: EX:
Write an assembly language program to generate B where b is the inverse of A.

## Slide 11: Solution:

## Slide 12
Thank You