University of Basrah – College of Engineering

Department of Civil Engineering

Subject:  Hydraulic Structures                                                      Exam: 2nd term

Class: Fourth year                                                                        Date : April 2017

Examiner: Prof. Dr.Saleh I. Khassaf                                          Time :1.5 Hours

Attempt All Questions

Q1] (35 Marks)

Design and sketch U.S.B.R. stilling basin for a given data of the hydraulic  structure:

Design discharge=1750 cumecs , width of water way=120m, crest level of the structure=30m and the sequent depth= 5.2m .

---------------------------------------------------------------------------------------------------------

Q2] (30 Marks)

Design and sketch a twin opening of an inverted siphon (8+27+6)m required to pass canal discharge of 3 cumecs under road with 0.18m head loss. The velocity in the canal is 0.78 m/sec and the depth water in the canal 1.4m , safety screen are provided of entry and exit. The inverted siphon has 22.5 degree elbows of each end , if n= 0.013 , k1=0.2 , k2=0.3 and kelbow=0.05 .

---------------------------------------------------------------------------------------------------------

Q3] (20 Marks)

- Drive the equation of the fiction losses in a square section of box culvert.

- What are the factors effecting  to select   the rip-rap. Sketch  the figure of the protection works at upstream and downstream of the hydraulic structure.

Q4] (15 Marks)

What are the functions of the following hydraulic structures with sketch.

- Vertical drop .

- Open aqueduct.

- End sill in stilling basin

GOOD LUCK

Prof. Dr. Saleh I. Khassaf                         Asst. Prof. Dr. Wisam  S. Al-Rekabi

Examiner                                                     Head of the Department