University of Basrah – College of Engineering

Department of Civil Engineering

Subject:  Hydraulic Structures                                                           Exam: Final

Class: Fourth year (Intensified Course)                                    Time: Two hours

Examiner: Prof. Dr.Saleh I. Khassaf                                               2022-2023

Attempt All Questions with assume any value if you need to solve any problem.

Q.1] ( 10+10) marks

A:  Given the following data for a hydraulic structure:

u.s.w.l.=120m , b.l.=115m , length of the floor=51m ,density of the concrete for the

floor=2400 kg/m3 , the gate at distance 15m from the upstream end , depth of cut-

off  5m  at downstream end .Calculate the thickness under the gate using Khosla’s

theory and draw the uplift pressure diagram.

B:  A head regulator at discharge 8 cumecs with upstream water depth 3m and downstream water depth 2.8m, the area of water way is 6m2 . If Cd =0.82. Find: (a) The velocity head .  (b)High opening of the regulator.

Q.2] (15marks)

A trapezoidal channel with bed width 7m and side slope 1:1 carries of water 10 cumecs , if the tail water depth in the canal is 1.5m , is the hydraulic jump will occur. Or not.? , if so design a suitable U.S.B.R. stilling basin with sketch.?

Q.3] (13 marks )

A concrete box culvert at two opening (2x3)m and (2x2)m , The total discharge of the structure is 16 cumecs , if the total length of the structure is 30m, k1=0.3 , k2=1 , n=0.015 . find the total head of the structure .sketch the structure.

Q.4] (12 marks)

Design a sliding steel gate for a barrage , if the stiffeners have an elastic modulus section equal to 500 cm3 , the clear water way of the barrage is 71.25m with 19 opening. each gate at height five meters, using fs=10000 ton/m2.

2-2