University of Basrah – College of Engineering

Department of Civil Engineering

Subject:  Hydraulic Structures                                                           Exam: Final

Class: Fourth year                                                                           Date: July 2020

Examiner: Prof. Dr.Saleh I. Khassaf                                               Fourth  attempt

Answer Five of the following questions  (20marks for each one)

Q.1]Fill the following blanks with a suitable statement :

1- A regulator is an example of control structure, While a dam is an example

of-----------.

2- If Froude number equal 2.5 , the type of flow is -----------.

3- The equation which used to calculate the critical depth in triangular

channel is ………….

4-the sum of water depth with velocity head is called ----------.

5-the piping occurs when the exit gradient is ----------critical gradient.

Q.2] Put true or false with correct the wrong one :

1- In  Bligh’s method , there is no idea of exit gradient.

2-Subcritical flow always occurs when the depth of flow is more than

The critical depth.

3-When downstream  depth is smaller than sequent depth, the hydraulic

jump can be control by rise the floor.

4-When the bed of canal is higher than the water level of valley, the crossing

structure which used is siphon.

5- A stone pitching is used to avoid the washout of bed material downstream

protection of any hydraulic structure.

Q.3] A horizontal concrete floor 15m length at a head 3m, the depth of cut-off 2m

at upstream end , and 1m at downstream end. Is the structure safe against

piping.?If not , design a safe one and calculate the thickness of the safe

structure using Lane’s method  (C=5) and draw the uplift pressure diagram.

Q.4] A hydraulic jump occurs in rectangular channel 6.1m wide , the rate of flow

22.6 cumecs, if the depth of water before jump is 0.47m . calculate the energy

dissipated of the jump. What’s the type of U.S.B.R. stilling basin of this

case.?

------------------------------------------------------------------------------------------------

Q.5]Calculate the thickness of plate for vertical gate in (inch) of a cross regulator

Which has two opening , the water way of the regulator is 5m and

the upstream water depth is 3.65m . Using fs=10000 psi and five division.

1-2

Q.6] Answer of the following questions:

- In major hydraulic structures cut-off walls used either one cut-off at upstream end of the floor or one cut-off at the downstream end or two cut-offs at both ends. Explain with sketches the functions and advantages of them for each position.?

- What’s the function of the vertical drop with sketch .?

C-What do you mean of crossing structures ? How to select each one .?

With my best wishes

2-2