## Slide 1
Electromagnetic surveying
Dr. Laurent Marescot
laurent@tomoquest.com

## Slide 2: Introduction
Electrical surveying…
Resistivity method
Induced polarization method (IP)
Self-potential (SP) method
Higher frequency methods (electromagnetic surveys):
Electromagnetic induction methods
Ground penetrating radar (GPR)

## Slide 4: Electromagnetic method
Electromagnetic (EM) surveying methods make use of the response of the ground to the propagation of electromagnetic field. This response vary according to the conductivity of the ground (in S/m).
Primary EM fields are generated using a alternating current in a loop wire (coil) or a natural EM source
The response of the ground is the generation of a secondary EM field
The resultant field is detected by the alternating currents that they induce in a receiver coil

## Slide 5: Application
Exploration of metalliferous mineral deposits
Exploration for fossil fuels (oil, gas, coal)
Engineering/construction site investigation
Glaciology, permafrost
Geology
Archaeological investigations

## Slide 6: Structure of the lecture
Equations in electromagnetic surveying
Survey strategies and interpretation
Conclusions

## Slide 7
1. Equations in electromagnetic surveying

## Slide 8: Maxwell equations
∂p
∇ ⋅ D = p or ∇ ⋅ j =
∇ ⋅ B = 0
Ampère − Maxwell
Faraday induction
∇ × E + ∂B = 0
∂t
∇ × H − ∂D = j
∂t
∂t
(Vs/m2 ) (A/m)
D displacement field (C/m2 )
j current density (A/m2 )
E electrical field (V/m)
B magnetic induction field
H magnetic field strenght
charge density (C/m3 )
p

## Slide 9: B and H fields
μ0 μ
B
H =
F = ev × B
μ = 4π10−7
0
(Vs/m2 )
⎛ Vs ⎞
permeability for vacuum
⎜ Am ⎟
μ permeability of material
B magnetic induction field
⎝ ⎠
Example of values for μ: Hematite, quartz: μ ≅1 Magnetite: μ ≅5
9
H
magnetic field strenght
(A/m)
We can measure B, not H!

## Slide 10: Frequencies
In the field, some frequencies are considered as noise and must be filtered out:
Light
CFF/SBB
3rd harmonic
50 Hz
16.6 Hz
150 Hz
T
ω = 2π f = 2π 1
f frequency (Hz)
T period (s)
ω angular velocity (rad/s)

## Slide 11: Basic theory: induction EM

## Slide 12: Basic theory: induction EM
∇ × E + ∂B = 0
∂t
∇ × H − ∂D = j
∂t
Ampère-Maxwell
Faraday

## Slide 13
Θ= π + φ = π + tan−1 (ωL / R)
2 2
R is the resistance of the conductor
L is the inductance of the conductor (or its tendancy to oppose a change
in the applied field)

## Slide 14: Real and imaginary components
14
S sinφ
S cosφ
in-phase component (real)
out-of-phase component (imaginary)
Θ = π + φ = π + tan−1 (ωL / R)
2 2

## Slide 15: Effect of a conductive body
15
Large conductivity (R → 0 and φ → π/2): Θ → π
Low conductivity (R → ∞ and φ → 0): Θ → π/2
Θ = π + φ = π + tan−1 (ωL / R)
2 2

## Slide 16: Tilt-angle methods
16
The receiving coil is turned until a null position is reached (no-signal): the plane of the coil then lies in the direction of
the arriving field

## Slide 17: Depth of penetration and skin depth
17
Skin depth:
depth δ at which the amplitude of the field reaches 1/e of its original value a the source
f
2ρ ρ
μ0ω
δ =
≈ 503
Depth of penetration: maximum depth ze at which a conductor
may still produce a recognizable EM anomaly (empirical relation)
σ f
ze ≈
100

## Slide 18
2. Survey strategies and interpretation

## Slide 19
Classification of EM methods
Uniform field methods
Magnetotelluric (MT)
Audio-magnetotelluric (AMT)
Very-Low Frequency (VLF-tilt, VLF-R)
Controlled source audio-magnetotelluric (CSAMT)
Dipolar field methods
Twin-coil or slingram systems: dipole source is used
Time-domain EM
Transient EM (TEM)

## Slide 20: Magnetotelluric (MT)
The source are fields of natural origin (magneto-telluric fields) resulting from flows of charged particles in the ionosphere, correlated with diurnal variations in the geomagnetic field caused by solar emissions
The only electrical technique capable of penetrating to the depths of interest to the oil industry (mapping salt domes and anticlines)
Frequencies range from 10-5 Hz to 20 kHz

## Slide 22: Telluric measurements
measured ellipse area (A22 )
unit base circle area (A )
1
2

## Slide 23
23
Map of A /A for a salt dome
2 1

## Slide 24: MT measurements
2
ωμ0 H y (ω )
Z (ω ) 2 =
ωμ0
1 Ex (ω )
1
ρ (ω ) =
a

## Slide 25: Audio-magnetotelluric (AMT)
Use equatorial thunderstorms as sources (1 to 20 kHz).
These EM fields are called sferics. Sferics propagated around the Earth between the ground and the ionosphere
The very broad frequency spectrum can be filtered to select a depth of investigation up to 1 km (AMT soundings)
Method sensitive to noise in urban areas

## Slide 26: AMT-MT sounding
2
0.2 ⎛ E ⎞
⎜ ⎟
⎝ H ⎠
ρ =
f
a

## Slide 28
28

## Slide 29: Very-Low Frequency (VLF-tilt)
29
Use submarine communication waves as sources (10 to 30 kHz). The transmitters are very powerful (>1 MW).The primary EM field is planar and horizontal
The depth of investigation mainly depends on the conductivity of rocks and the transmitter chosen (from 10m to 100m)
Disadvantages: transmission frequently broken, difficult to find a transmitter in an appropriate direction
Advantages: light, fast and easy to use

## Slide 30: VFL-tilt measurements
30

## Slide 31: VFL-tilt measurements

## Slide 32: Very-Low Frequency (VLF-R)
Gives apparent resistivity of the ground and phase shift by measuring H and E
Various local radio waves can be used to chose a depth of investigation (frequency can be chosen)

## Slide 33: VLF-R measurements
2
0.2 ⎛ E ⎞
⎜ ⎟
⎝ H ⎠
ρ =
f
a

## Slide 34: Controlled source AMT (CSAMT)
Similar to MT but using a remote (2 to 8 km) electrical dipole as source (1 Hz to 10 kHz)
The source frequency and location is known

## Slide 35: CSAMT measurements

## Slide 36: Dipole-source methods
Measurements tolls called twin-coil or slingram systems
Tx and Rx are coils (about 1m diameter) linked by a cable which carries a reference signal in order to compensate the effect of the primary field. By this means, the system subsequently responds only to the secondary fields
A decomposer spilt the secondary field into real and imaginary components (display the result as a percentage of the primary field)

## Slide 38
38
EM31 (Geonics), 9.8 kHz, s=3.66 m
EM34 (Geonics),
6.4 kHz for s=10 m
1.6 kHz for s=20 m
0.4 kHz for s=40 m
EM38 (Geonics), 14.6 kHz, s=1 m
s: Rx-Tx distance

## Slide 41: EM at low induction numbers (LIN)
Depth of investigation depends on the distance Tx-Rx
The response is proportional to ground conductivity
Manufacturer adapts the Rx-Tx distance (s) and frequency ( f ) for a LIN approximation, i.e. s<<δ:
ρ
δ ≅ 503
is the induction number
N = s / δ
a
f
B
P
N << 1 ⇒ H S
B
H iμ ωσs2
≅ σ
0
4

## Slide 42
CST and VES using LIN
CST: moving vertical and horizontal dipoles with various constant depth (survey principle similar to resistivity CST and tomography)
VES: increasing Tx-Rx spacing around a same location point and using vertical and horizontal dipoles (survey principle similar to resistivity VES)

## Slide 44
44

## Slide 45
45

## Slide 46: Transient EM (TEM)
TEM uses a primary field which is not continuous but consists of a series of pulses separated by measurement periods when the transmitter is inactive
Primary and secondary fields are clearly separated
Investigation depth up to several km could be achieved, but difficult to use in shallow geophysics (no reliable information in the 0-10 m depth range)

## Slide 47: TEM measurements

## Slide 48: TEM measurements

## Slide 50
50

## Slide 52: Remarks on interpretation
Indirect approach using theoretical computations of simple geometry shapes (spheres, cylinders, thin sheets, horizontal layers)
Laboratory modeling (using special scaling rules)
Use of master curves for simple Earth structures
Mainly qualitative. Quantitative inversion in development, soundings very used

## Slide 53
3. Conclusions

## Slide 54: Advantages
Surveys are easy to carry out, non-expensive (require less field operators than resistivity methods)
Rapid qualitative overview
No galvanic coupling with the ground required
Theoretically less sensitive to non-unicity in the solution than resistivity

## Slide 55: Drawbacks
Quantitative interpretation of EM anomalies is complex
Penetration not very great if very conductive superficial layers are present