## Slide 1
Process Control
Course II
Lecture 11
Process Control Loops
Part I
By
Prof. Alaa Kareem Mohammed

## Slide 2
Outline
4 - Line symbols
3- Tag descriptor
5- Instrument Location
6- Instrumentation Numbering
2- Basic control Loop
1- Project Diagrams

## Slide 3
1- Project Diagrams
Block Diagram
BD
Process Flow Diagram
PFD
Piping & Instrumentation Diagram
PID

## Slide 4
Block Diagram BD
Reactor
Gas Separator
Toluene, C7H8 10,000 kg/hr
Hydrogen H2 820 kg/hr
Mixed Liquid
75% Conversion of Toluene
Mixed Gas 2610 kg/hr
Benzene, C6H6 8,210 kg/hr
C6H6
CH4
C7H8

## Slide 5
Stream Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Temperature (oC) | 25.0 | 35.0 | 35.0 | 35.0 | 35.0 | 60.3 | 41 | 38 | 54 | 45.1
Pressure (psi) | 28 | 32.2 | 31.0 | 31.0 | 30.2 | 45.1 | 31.3 | 24.0 | 39 | 2.6
Vapor fraction |  |  |  |  |  |  |  |  |  | 
Mass flow (tonne/hr) | 10.3 | 13.3 | 0.82 | 20.5 | 6.41 | 20.5 | 0.36 | 9.2 | 20.9 | 11.6
Mole flow (kmol/hr) | 108 | 114.2 | 301.0 | 1204.0 | 758.8 | 1204.4 | 42.6 | 1100.8 | 142.2 | 244.0
25
28
35
32.2
35
31.0
38
20
T-100
Distillation Column
Ethanol
H2SO4
Ethylene
Ethylene liq.
Ethane
Ni
Hydrogen
Cold water in
Hot water out
H2O
R-100
Reactor
E-100
Condenser
R-101
Reactor
R-100
T-100
E-100
R-101
P-100
Pump
P-101
Pump
1
2
3
4
5
6
7
8
9
10
V-101
V-102
V-103
CV-100
V-100
V-104
V-105
V-106
V-107
CV-101
P-100
P-101
Process Flow Diagram PFD

## Slide 6
Piping & Instrumentation Diagram PID

## Slide 7
m
cp
Ti
Steam in
m
cp
To
M
Q
Process
T T
Tc
Set point
2- Basic Control Loop
Consider the continuous stirred tank heater CSTH which shown below. We wish to maintain the outlet stream at a certain temperature value To. The system contains the control loop which consists of the following elements:
1- Temperature measuring element.
2- Temperature transmitter.
3- Temperature controller.
4- Control valve.

## Slide 8
In general , the basic loop consists of the following element that shown in Figure below.
Process
Sensing Element
Measuring
Element
Transmit
Element
Control Element
Final Control
Element
Transmitter

## Slide 9
Transmitter
Controller
Orifice
(Flow Sensor)
Set point
Fluid
Fluid
Control valve
F T
FIC
Set point
F E
C V

## Slide 10
m
cp
Ti
Steam in
m
cp
To
M
Q
Process
T T
Tc
Set point
m
cp
Ti
Steam in
m
cp
To
M
Q
Process
T T
TC
Set point
T E
TR
m
cp
Ti
Steam in
m
cp
To
M
Q
Process
T T
TRC
Set point
T E

## Slide 11
The tag descriptor may be written as :
X Y Z
X Z
or
Where:
X refers to variable
Y refers to function
Z refers to instrument
Variable | Symbol
Temperature | T
Pressure | P
Flow | F
Level | L
Acidity | pH
Function | Symbol
Recording | R
Indicating | I
Control | C
Deferential | D
Instrument | Symbol
Indicator | I
recorder | R
Controller | C
Transmitter | T
Switch | S
Valve | V
Element | E
Alarm | A
X
Y
Z
pH E
LS
FRC
TI
PCV
Temperature Indicator
Flow Recording Controller
Level switch
pH Element
Pressure Control Valve
3- Tag descriptor

## Slide 12
TI
Temperature Indicator
TR
Temperature Recorder
TC
Temperature Controller
TT
Temperature Transmitter
TE
Temperature Element
TIC
Temperature indicating Controller
TRC
Temperature recording Controller
TCV
Temperature Control valve
TA
Temperature Alarm
TS
Temperature Switch
Temperature

## Slide 13
FI
Flow Indicator
FR
Flow Recorder
FC
Flow Controller
FT
Flow Transmitter
FE
Flow Element
FIC
Flow indicating Controller
FRC
Flow recording Controller
FCV
Flow Control valve
FA
Flow Alarm
FS
Flow Switch
Flow

## Slide 14
PI
Pressure Indicator
PR
Pressure Recorder
PC
Pressure Controller
PT
Pressure Transmitter
PE
Pressure Element
PIC
Pressure indicating Controller
PRC
Pressure recording Controller
PCV
Pressure Control valve
PA
Pressure Alarm
PS
Pressure Switch
Pressure

## Slide 15
LI
Level Indicator
LR
Level Recorder
LC
Level Controller
LT
Level Transmitter
LE
Level Element
LIC
Level indicating Controller
LRC
Level recording Controller
LCV
Level Control valve
LA
Level Alarm
LS
Level Switch
Level

## Slide 16
4- Line symbols
Process Connection
Electrical Signal
Data link
Electromagnetic or
sonic signal
Capillary tube
Pneumatic signal
Hydraulics signal

## Slide 17
5- Instrument Location
- Instruments that are mounted on the equipment or in the pipe network.
(i.e. sensor that mounted on pipeline or process equipment.)
Field mounted on pipeline

## Slide 18
Instrument that located on central control panel.
Front mounted ( visible to the operator)

## Slide 19
- Instrument that located on central control panel.
- Rear mounted (invisible to the operator. Instruments that are mounted behind a control panel board.

## Slide 20
Shared instrument that located on central control panel shared in Distributed Control System (DCS)
- The entire system of controllers is connected by networks for communication and monitoring.

## Slide 21
- The instrument is mounted on the local control panel near the equipment,
- Front mounted (visible to the operator).

## Slide 22
- The instrument is mounted on the local control panel near the equipment,
- Rear mounted (invisible to the operator).

## Slide 23
Field mounted
The instrument is mounted on the equipment or on the pipe.
Main control panel front-mounted.
The instrument is mounted in the remote panel, visible to the operator
Main control panel rear-mounted.
The instrument is mounted in the remote panel, invisible to the operator( behind the panel)
Auxiliary control panel front –mounted.
The instrument is mounted on the local panel near the equipment, visible to the operator.
Auxiliary control panel rear - mounted
The instrument is mounted on the local panel near the equipment, invisible to the operator( behind the panel).
Main control panel front-mounted.
Shared instrument is mounted in the remote panel, visible to the operator

## Slide 24
Example 1
Steam in
Q
Set point
H
m , T2
T E
TR
T I
Tc
m , T1
LI
LE
LRC
LT
Describe the control instrument in the diagram below.

## Slide 25
6- Instrument Numbering
XYZ NRR LL
Where:
X refers to variable. T=Temperature, P = Pressure ……etc.
Y refers to function. R = Recording, I = Indicating………etc.
Z refers to instrument. C =Controller. E= Element ………etc.
NRR : Number of instrument
N : Zone No. in the plant.
LL : Control loop No.
For example
TRC
10520
Temperature Recording Controller
No.: 105
Zone :1
Loop No. : 20

## Slide 26
Exercise
Describe the following instruments
PIC
34510
LS
255 30
TS
20916
FA
45115

## Slide 27
Example 2
Consider the storage tank T-101 shown below. Construct a control loop according to the following specification:
1- Level element
2- Level transmitter
3- Level indicator: located on remote control panel (visible)
4- Level recording controller. (function in DCS)
5- Pneumatic control valve
6- Zone No. =2
7- loop No. 4
7- Label each instrument with a number 16.
h
q1
q2
T-101
R

## Slide 28
Solution
h
q2
L E
L T
q1
LI
LRC
21604
21604
21604
21604
R

## Slide 29
Example 3
Consider the pressurized vessel (V-101) below. Draw control loop to show that the solenoid valve SV-100 will be activated to relief pressure when the pressure in the V-101 is higher than the desired value. Use the following instruments
1- Pressure element locally mounted.
2- Pressure transmitter locally mounted.
3- Pressure indicating controller that is function in DCS.
3- Suggest numbers for instruments.
V-101
SV -100
F1
Gas inlet
Relief gas
F2
S

## Slide 30
Solution
P IC
P E
10307
V-101
SV -100
F1
Gas inlet
Relief gas
F2
P T
10307
10307
S

## Slide 31
Example 4
(pH adjustment tank)
TK-100
Base tank
Acid tank
TK-101
TK-102
S
S
F1
Inlet solution
outlet solution
F2
SV-101
SV-102
H2SO4
NaOH
The diagram below shows pH adjustment.
We want to keep the solution in the tank TK-100 at pH=6.
When pH of the solution reduced below 6, Solenoid valve SV-101 will be opened to dosing NaOH to the tank TK-100.
When the pH become higher than 6, SV-102 will be opened to dosing H2SO4 to the tank TK-100.
Use two control loops, each loop contains element, transmitter , indicating controller (mounted on local panel)

## Slide 32
Solution
(pH adjustment tank)
TK-100
Base tank
Acid tank
TK-101
TK-102
S
S
F1
Inlet solution
outlet solution
F2
SV-101
SV-102
H2SO4
NaOH
10706
pHE
pHT
pHIC
10807
10807
10807
pHE
pHIC
pHT
10706
10706

## Slide 33
Homework
Consider the system below which consists of two liquid- level tanks connected in series. The two levels h1 and h2 are to be controlled.
h1
h2
LCV101
LCV102
qo
q1
q2
Draw two control loops, each one consists of Element, transmitter , indicator (local panel) and level recording controller (function in DCS).
Give a number for each loop.
TK101
TK102

## Slide 34
Thank you
Any ?