Freehand Sketching

The freehand is the first step to the preparation of a scale drawing.

A designer records his idea initially in the form of sketches which are later converted into drawing.

Sketching Qualities

- Made in correct proportion but not to scale.

- All features of the object, together with their dimension, etc, clearly incorporated.

Sketching materials

- Soft grade pencil.

- Soft rubber eraser.

- Paper in the form of sketch book.

Prepare the sketching

- Determine the over all dimension

- Draw a rectangular proportional to the overall dimension which contains the drawing or by draw two lines one perpendicular to the other which equal proportionally to width and height of figure respectively.

- Insert the centre lines for arcs and circles and block-in the main shapes.

- Sketch the circles and arcs and build up the details.

- Erase all construction lines and insert all dimensions.

To sketch Straight Lines:

Horizontal lines are sketched with the motion of wrist and the fore-arm. While vertical lines are sketched downwards with the movement of fingers.

To sketch circles and arcs:

- Mark the centre and through it

- Draw horizontal and vertical centre lines.

- Add four radial lines between them.

- Mark points on theses lines at radius distance from the centre.

- Sketch small arcs through these points.

(Hint: For large circles adding a few extra radial lines).

Worked Example

- Using freehand sketching method to draw the front, top and side views in first angle projection, for the figure (1), add all dimensions.

Question

- How to sketch the large circle and arc. Explain with the aid of freehand sketch.

- What is the benefit of using freehand sketch and how it differs from the scale drawing in general?