## Slide 1: Lab 4: Industrial Pharmacy II wet granulation method
Presented by
Assistant Lecturer: Aula Jawad

## Slide 2: Steps of Wet Granulation

## Slide 3
weighing and mixing of the ingredients
  Specified amounts of active ingredients, fillers, and disintegrating agents are mixed until a homogeneous mixture is formed
Preparing a damp mass
  A liquid binder is subsequently added to the powder mixture to facilitate agglomeration of the powder particles.
  A damp mass resembling a dough is formed and further processed into granules.
  The amount of binding agent added is usually determined by the formation of wet compact mass. (ball test)
  However, care must be taken not to over-wet the power as over-wetting causes???
  The length of wetting time depends on the???

## Slide 4
  3. Converting the damp mass into wet granules
  The wet mass is forced through a screen to form wet granules.
4. Drying the granules
The resultant wet granules are spread evenly on a large piece of paper for drying.
Avoid over-drying the granules as it causes??
5- Dry screening
After drying; then dry screening is performed to get homogenized granules with uniform size and shape.

## Slide 5
6- Mixing
By addition of lubricants and glidants.
Therefore, the granules will possess
good compressibility
good flowability
Finally, compression into tablet

## Slide 6: Advantages of the wet granulation method:
1. Improve flowability, cohesiveness, and compressibility of the powder, so the powder is easily compressed with lower binder concentration
2. Can be used for high-dose drugs with weak compressibility that is not affected by heat and moisture.
3. Maintaining uniform distribution for low-dose drug and water-soluble dyes (coloring agents).
4. Improve the dissolution rate of the hydrophobic drug because of the presence of moisture in the already used water.
5. Maintaining good content uniformity due to prevention of particle segregation since all the granules will have the same density.

## Slide 7: Disadvantages of the wet granulation method
1. cost-time consumer
2. Personal and environmental hazards upon using organic solvents are represented by the flammability and toxicity of these solvents after evaporation during drying, handling, or storage.
3. Stability problem because the presence of moisture speeds up the reaction between active ingredients and the additives and the additives themselves.

## Slide 8: Preparation of Ibuprofen tablet by wet granulation method
Ibuprofen 400 mg 4.8 g
MCC 200 2.4 g
Ethanol q.s
Mg stearate 1%
Prepare 12 tab

## Slide 9: procedure
1. Weigh the required amount of active ingredients and excipients except lubricant and mix them
2. Add the binder solution (pvp 10%) drop by drop until a wet mass is obtained (ball test)
3. Calculate the amount of binder used (pvp solution 10%)
4. The wet mass is forced through a sieve 8 by hand to prepare the wet granules.
5. The resultant granules are dried for 5 minutes in a hot air oven
6. After drying, the granules are passed through a sieve 20 and weight the granules after sieving.
7. Add the required amount of lubricant (1%) and mix for 2 minutes.
8. Compress into a tablet