## Slide 1
Titrations
Introduction
  1.) Buret Evolution
    Primary tool for titration
Descroizilles (1806)
Pour out liquid
Gay-Lussac (1824)
Blow out liquid
Henry (1846)
Copper stopcock
Mohr (1855)
Compression clip
Used for 100 years
Mohr (1855)
Glass stopcock

## Slide 2
Titrations
Introduction
  2.) Volumetric analysis
    Procedures in which we measure the volume of reagent needed to react with an analyte
  3.) Titration
    Increments of reagent solution (titrant) are added to analyte until reaction is complete.
      - Usually using a buret
    Calculate quantity of analyte from the amount of titrant added.
    Requires large equilibrium constant
    Requires rapid reaction
      - Titrant is rapidly consumed by analyte
Controlled Chemical Reaction

## Slide 3
Titrations
Introduction
  4.) Equivalence point
    Quantity of added titrant is the exact amount necessary for stoichiometric reaction with the analyte
      - Ideal theoretical result
Analyte
Oxalic acid
(colorless)
Titrant
(purple)
(colorless)
(colorless)
Equivalence point occurs when 2 moles of MnO4- is added to 5 moles of Oxalic acid

## Slide 4
Titrations
Introduction
  5.) End point
    What we actually measure
      - Marked by a sudden change in the physical property of the solution
      - Change in color, pH, voltage, current, absorbance of light, presence/absence ppt.
CuCl Titration with NaOH
Before any addition of NaOH
After the addition of 8 drops of NaOH
End Point

## Slide 5
Titrations
Introduction
  5.) End point
    Occurs from the addition of a slight excess of titrant
      - Endpoint does not equal equivalence point
Analyte
Oxalic acid
(colorless)
Titrant
(purple)
(colorless)
(colorless)
After equivalence point occurs, excess MnO4- turns solution purple  Endpoint

## Slide 6
Titrations
Introduction
  5.) End point
    Titration Error
      - Difference between endpoint and equivalence point
      - Corrected by a blank titration
      i. repeat procedure without analyte
      ii. Determine amount of titrant needed to observe change
      iii. subtract blank volume from titration
    Primary Standard
      - Accuracy of titration requires knowing precisely the quantity of titrant added.
      - 99.9% pure or better  accurately measure concentration
Analyte
Oxalic acid
(colorless)
Titrant
(purple)

## Slide 7
Titrations
Introduction
  6.) Standardization
    Required when a non-primary titrant is used
      - Prepare titrant with approximately the desired concentration
      - Use it to titrate a primary standard
      - Determine the concentration of the titrant
      - Reverse of the normal titration process!!!
titrant known concentration
analyte unknown concentration
titrant unknown concentration
analyte known concentration
Titration
Standardization

## Slide 8
Titrations
Introduction
  7.) Back Titration
    Add excess of one standard reagent (known concentration)
      - Completely react all the analyte
      - Add enough MnO4- so all oxalic acid is converted to product
    Titrate excess standard reagent to determine how much is left
      - Titrate Fe2+ to determine the amount of MnO4- that did not react with oxalic acid
      - Differences is related to amount of analyte
      - Useful if better/easier to detect endpoint
Analyte
Oxalic acid
(colorless)
Titrant
(purple)
(colorless)
(colorless)

## Slide 9
Titrations
Titration Calculations
  1.) Key – relate moles of titrant to moles of analyte
  2.) Standardization of Titrant Followed by Analysis of Unknown
Calculation of ascorbic acid in Vitamin C tablet:
Starch is used as an indicator: starch + I3-  starch-I3- complex
(clear) (deep blue)
(ii) Titrate ascorbic acid with I3-:
1 mole ascorbic acid  1 mole I3-

## Slide 10
Titrations
Titration Calculations
  2.) Standardization of Titrant Followed by Analysis of Unknown
Standardization: Suppose 29.41 mL of I3- solution is required to react with 0.1970 g of pure ascorbic acid, what is the molarity of the I3- solution?

## Slide 11
Titrations
Titration Calculations
  2.) Standardization of Titrant Followed by Analysis of Unknown
Analysis of Unknown: A vitamin C tablet containing ascorbic acid plus an inert binder was ground to a powder, and 0.4242g was titrated by 31.63 mL of I3-. Find the weight percent of ascorbic acid in the tablet.

## Slide 12
Titrations
Spectrophotometric Titrations
  1.) Use Absorbance of Light to Follow Progress of Titration
    Example:
      - Titrate a protein with Fe3+ where product (complex) has red color
      - Product has an absorbance maximum at 465 nm
      - Absorbance is proportional to the concentration of iron bound to protein
Analyte
(colorless)
(red)
titrant
(colorless)
As Fe3+ binds protein
solution turns red

## Slide 13
Titrations
Spectrophotometric Titrations
  1.) Use Absorbance of Light to Follow Progress of Titration
    Example:
      - As more Fe3+ is added, red color and absorbance increases,
      - When the protein is saturated with iron, no further color can form
      - End point – intersection of two lines (titrant has some absorbance at 465nm)
As Fe3+ continues to bind protein
red color and absorbance increases.
When all the protein is bound to Fe3+,
no further increase in absorbance.

## Slide 14
Titrations
Spectrophotometric Titrations
  1.) Use Absorbance of Light to Follow Progress of Titration
    Example:
      - As more Fe3+ is added, concentration changes due to dilution
      - Need to correct absorbance for dilution.
Total volume changes after each addition

## Slide 15
Titrations
Precipitation Titration Curve
  1.) Graph showing how the concentration of one of the reactants varies as titrant is added.
    Understand the chemistry that occurs during titration
    Learn how experimental control can be exerted to influence the quality of an analytical titration
      - No end point at wrong pH
      - Concentration of analyte and titrant and size of Ksp influence end point
      - Help choose indicator for acid/base and oxidation/reduction titrations
Sharpness determined by titration condition
Monitor pH, voltage, current, color, absorbance, ppt.

## Slide 16
Titrations
Precipitation Titration Curve
  2.) Because concentration varies over many orders of magnitude, plot p function
  3.) Example:
p function:
where [X] is concentration of X
Consider the titration of 25.00 mL of 0.1000M I- with 0.05000M Ag+
Since Ksp is so small, each addition of Ag+ reacts completely with I-

## Slide 17
Titrations
Precipitation Titration Curve
  3.) Example:
At equivalence point, sudden increase in Ag+ concentration.
- All I- has been consumed
What volume (Ve) of Ag+ titrant is need to reach the equivalence point?
mol I-
mol Ag+
One mole of Ag+ reacts with one mol I-

## Slide 18
Titrations
Precipitation Titration Curve
  4.) Three distinct regions in titration curve
    Before, at and after the equivalence point.
    Before the Equivalence Point
      - All titrant [Ag+] is consumed, free [I-] is [I-] that has not been precipitated.
      - Negligible I- from AgI(s) (Ksp)
before
after
at
Moles of I- = original moles of I- - moles of Ag+ added

## Slide 19
Titrations
Precipitation Titration Curve
  4.) Three distinct regions in titration curve
    Before the Equivalence Point
      - Concentration of Ag+ is governed by Ksp
Consider the titration of 25.00 mL of 0.1000M I- with 10 mL of 0.05000M Ag+
Moles of I- = original moles of I- - moles of Ag+ added
Volume is 0.3500 L ( 25.00 mL + 10.00 mL)
Concentration of Ag+ in equilibrium with this much I-

## Slide 20
Titrations
Precipitation Titration Curve
  4.) Three distinct regions in titration curve
    Before the Equivalence Point
      - Concentration of Ag+ is governed by Ksp
    At Equivalence Point
    - added exactly enough Ag+ to react with all I-
    - [Ag+] independent of the original concentrations
    - [Ag+] dependent on Ksp
p function
2 sig. fig.  2 sig. fig. in the mantissa of p function

## Slide 21
Titrations
Precipitation Titration Curve
  4.) Three distinct regions in titration curve
    After Equivalence Point
    - All Ag+ added before equivalence point has ppt.
    - [Ag+] is determined by Ag+ added after the equivalence point.
    > volume after equivalence point
For 2 mL of Ag+ added past equivalence point

## Slide 22
Titrations
Shape of Titration Curve
  1.) Equivalence point is the steepest point of the curve.
    Point of maximum slope  inflection point  second derivative is zero

## Slide 23
Titrations
Shape of Titration Curve
  2.) Affect of Ksp on Titration Curve.
    Lowest solubility gives steepest change at equivalence point
Magnitude of concentration change and ease of identifying equivalence point increases with Ksp

## Slide 24
Titrations
Titration of a Mixture
  1.) Product with the Smaller Ksp Precipitates First
    Two Stage Titration Curve
      - Assumes significant difference in Ksp
Titrate Mixture of KI and KCl with AgNO3
Ksp(AgI) << Ksp(AgCl)
First, AgI ppt.
Then, AgCl ppt.
AgI ppt. not complete at midpoint

## Slide 25
Titrations
End-Point Detection
  1.) Precipitation Titration
    End points detected with electrode or indicator
      - Electrode – converts concentration of specific ion into measurable current or
      potential.
      - Indicators:
      Volhard titration: formation of a soluble, colored complex at the end point
      Fajans titration: adsorption of a colored indicator on the precipitate at the end
      point
pH electrode responds to [H+]

## Slide 26
Titrations
End-Point Detection
  1.) Precipitation Titration
    Volhard titration (First Published in 1874)
Determine [Cl-]:
First ppt. Cl- by titration with Ag+ and filter off solid
Titrate excess Ag+ with thiocyanate (SCN-)
When all Ag+ is consumed, thiocyanate binds Fe3+. Appearance of Red color is endpoint
Total amount of Ag+ is known, so amount consumed by Cl- can be calculated
Subtract excess [Ag+] from total [Ag+] used to ppt. Cl-

## Slide 27
Titrations
End-Point Detection
  1.) Precipitation Titration
    Fajans titration
    - Uses an adsorption indicator
Precipitate surface is initially negatively charged due to excess Cl-
AgCl ppt.
After equivalence point (end point), have excess Ag+ so surface is now positively charged.
Anionic dye is attracted to positive charged surface. Adsorption of dye causes color change
AgCl ppt.

## Slide 28
Titrations
End-Point Detection
  1.) Precipitation Titration
    Fajans titration
    Anionic dyes
    - Maximize surface area  higher binding stronger color change
    - small particle size  low concentration
    - must use appropriate pH to maintain negative charge
Changes from greenish yellow to pink
Sharper color transition, binds to tightly to Cl-

## Slide 29
Titrations
End-Point Detection
  2.) Typical Applications
    Also indicates potential sources of interference
    - other ions/analytes may be present in sample