## Slide 1: Chapter One Elasticity

## Slide 2: Elastic Properties of Materials
Stress
Strain
Young’s Modulus
Hooke’s Law

## Slide 3: Elasticity
An elastic body is one that returns to its original shape after a deformation.
Rubber Band

## Slide 4
An inelastic body is one that does not return to its original shape after a deformation.
Clay

## Slide 5: Elastic or Inelastic?
An elastic collision loses no energy. The deformation on collision is fully restored.
In an inelastic collision, energy is lost and the deformation may be permanent.

## Slide 6: Stress and Strain
stress: describes the applied forces
strain: describes the resulting deformation
modulus: property of material under stress
(large modulus means small deformation)
Hooke’s Law: stress = modulus × strain

## Slide 7: Types of Stress and Strain
Applied forces are perpendicular to surface:
tensile stress
bulk (volume) stress
Applied forces are parallel to surface:
shear stress

## Slide 8: Tensile Stress and Strain
tensile stress = F/A
tensile strain = Dl/l0
Young’s modulus = Y

## Slide 9
Tensile of Stress : is the force per unit area producing elongation of an object.
=
F:Force applied in Newton
A:cross sectional area in m2
 : Stress in N/m2
A
A
F
Tensile

## Slide 10: Strain :Ratio of elongation of material to the original length
 =, where :  l : elongation(m), l o : original length of a material (m) and  is strain ,Dimensionless.
Elongation l =l – lo
Where : l loaded length of a material(m)
l
lo

## Slide 11
Shear of Stress : is the opposite “sliding force “ applied to parallel force of the object . Producing change in shape of material without changing its volume
Shear
F
F

## Slide 12: Shear Stress and Strain

## Slide 13: Shear Stress and Strain
shear stress = F7/A
shear strain = x/h = tanf
shear modulus = S

## Slide 14: Shear Stress and Strain

## Slide 15: Deformation types and define an elastic modulus
1.Young’s modulus(Y) ,which measures the resistance of a solid to a change in its length.
نتوقع معامل يونح للحديد اكبر من معامل يونج للمطاط
2. Bulk modulus(B) , which measures the resistance of solider or liquids to changes in their volume.
3. Shear modulus(S) ,which measures the resistance to motion of the planes within a solid parallel to each other.

## Slide 16
Young's modulus (E or Y) :
is a measure of a solid's stiffness or resistance to elastic deformation under load. It relates stress (force per unit area) to strain (proportional deformation) along an axis or line. The basic principle is that a material undergoes elastic deformation when it is compressed or extended, returning to its original shape when the load is removed. More deformation occurs in a flexible material compared to that of a stiff material. In other words:
A low Young's modulus value means a solid is elastic.
A high Young's modulus value means a solid is inelastic or stiff.

## Slide 17: Units
stress = modulus × strain
stress (‘applied force’): pascal= Pa=N/m2
strain (‘deformation’): dimensionless
modulus: same unit as stress

## Slide 18: Young’s Modulus : Elasticity in Length
Y= = Young’s modulus
Young’s modulus is typically used to characterize
a rod stressed under either tension or compression .

## Slide 19: Bulk Stress and Strain
pressure: p=F/A
bulk stress = Dp
bulk strain = DV/V0
bulk modulus = B

## Slide 20: Bulk Modulus : Volume Elasticity
B = = = - Bulk modulus
-A negative sign is inserted in this defining equation so that B is a positive number . This maneuver necessary because an increase in pressure ( positive P) cause a decrease in volume ( negative V) and vice versa.

## Slide 21: Shear Modulus :Elasticity of Shape
A
F
F
f
l
d
A shearing stress alters only the shape of the body, leaving the volume unchanged. For example, consider equal and opposite shearing forces F acting on the cube below:
The shearing force F produces a shearing angle . The angle  is the strain and the stress is given by F/A as before.

## Slide 22: Calculating Shear Modulus
F
F
f
l
d
A
The strain is the angle expressed in radians:
Stress is force per unit area:
The shear modulus S is defined as the ratio of the shearing stress F/A to the shearing strain :
The shear modulus: Units are in Pascals.

## Slide 27
ناقش إمكانية حدوث كسر في عظمتي ساق يبلغ طولهما الإجمالي حوالي 90 سم ومساحتهما المتوسطة حوالي 6 سم2 عندما يقفز شخص يزن 70 كجم من ارتفاع 60 سم
.

## Slide 28: Relation between Stress and Strain
The relation between the stress and the strain for a material under tension can be found experimentally .
A plot of stress vs. strain .
The diagram gives us the behavior of the material and material properties

## Slide 29: Regimes of Deformation
O to a :
(small stress, strain)
stress=modulus × strain
elastic, reversible
a < b :
elastic, reversible
but stress and strain not proportional

## Slide 30: Regimes of Deformation
From point O to b :
elastic, reversible
from point b to d:
plastic, irreversible
ductile materials have long c–d curves
brittle materials have short c–d curves

## Slide 31
substance | Young’s Modulus (N/m2) | Shear Modulus (N/m2) | Bulk Modulus (N/m2)
Tungsten | 35x1010 | 14x1010 | 20x1010
Steel | 20x1010 | 8.4x1010 | 6x1010
Copper | 11x1010 | 4.2x1010 | 14x1010
Brass | 9.1x1010 | 3.5x1010 | 6.1x1010
Aluminum | 7.0x1010 | 2.5x1010 | 7.0x1010
Glass | 6.5-7.8x1010 | 2.6-3.2x1010 | 5.0-5.5x1010
Quartz | 5.6x1010 | 2.6x1010 | 2.7x1010
Water | --------- | ------- | 0.21x1010
Mercury | --------- | ------- | 2.8x1010
Typical Values for Elastic Modulus

## Slide 32
Deformations Summary Table
Bulk Modulus (B)
Shear modulus (S)
Young’s modulus (Y)
Constant of proportionality
Fractional change in volume
Ratio of the relative displacement to the separation of the two parallel surfaces
Fractional change in length
Strain
Pressure
Shear force divided by the area of the surface on which it acts
Force per unit cross-sectional area
Stress
Volume
Shear
Tensile or compressive

## Slide 33
Exercise

## Slide 34
Example:A 108N/m2 stress produces a strain 5x10-4. What is Young’s modulus for this bar?
Given: = 108 N/m2;  = 5x10-4
Young’s modulus
20x1010 N/m2

## Slide 35: Example : A steel wire 10 m long and 2 mm in diameter is attached to the ceiling and a 200-N weight is attached to the end. What is the applied stress?
L
DL
A
A
F
First find area of wire:
A = 3.14 x 10-6 m2
Stress
6.37 x 107 Pa

## Slide 36: Example : A 10 m steel wire stretches 3.08 mm due to the 200 N load. What is the longitudinal strain?
Given: L = 10 m; DL = 3.08 mm
Longitudinal Strain
3.08 x 10-4
L
DL

## Slide 37
Example :
How much pressure is needed to compress the volume of an iron block by 0.10 percent ? Express answer in N/m2 , and compare it to atmospheric pressure (1.0x105 N/m2) ?
Yong’s modulus for iron (90x1010 N/m2 )
Solution :
B = -
=
Then : 90x1010 = -
P= 90x106 N/m2

## Slide 38
Example : The upper surface of a cube of gelatin, 5.0 cm on a side, is displaced by 0.64 cm by a tangential force. The shear modulus of the gelatin is 940 Pa. What is the magnitude of the tangential force?
F
F
From Hooke’s Law:

## Slide 39
Example : An anchor, made of cast iron of bulk modulus 60.0109 Pa and a volume of 0.230 m3, is lowered over the side of a ship to the bottom of the harbor where the pressure is greater than sea level pressure by 1.75106 Pa. Find the change in the volume of the anchor.

## Slide 40
Example: A steel beam is placed vertically in the basement of a building to keep the floor above from sagging. The load on the beam is 5.8104 N and the length of the beam is 2.5 m, and the cross-sectional area of the beam is 7.5103 m2. Find the vertical compression of the beam.
Force of floor on beam
Force of ceiling on beam
For steel Y = 200109 Pa.

## Slide 41: Example : A hydrostatic press contains 5 liters of oil. Find the decrease in volume of the oil if it is subjected to a pressure of 3000 kPa. (Assume that B = 1700 MPa.)
DV = -8.82 mL
Decrease in V; milliliters (mL):

## Slide 42: Example : The stress applied to the steel wire was 6.37 x 107 Pa and the strain was 3.08 x 10-4. Find the modulus of elasticity for steel.
L
DL
Y = 207 x 109 Pa
This longitudinal modulus of elasticity is called Young’s Modulus and is denoted by the symbol Y.

## Slide 43: Example: A steel stud (S = 8.27 x 1010Pa) 1 cm in diameter projects 4 cm from the wall. A 36,000 N shearing force is applied to the end. What is the defection d of the stud?
d
l
F
Area: A = 7.85 x 10-5 m2
d = 0.222 mm

## Slide 45: Hooke’s Law
When a spring is stretched, there is a restoring force that is proportional to the displacement.
F = -kx
The spring constant k is a property of the spring given by:
F
x
m
The spring constant k is a measure of the elasticity of the spring.

## Slide 46: Hook’s Law
An Elastic Spring
A spring is an example of an elastic body that can be deformed by stretching
A restoring force, F, acts in the direction opposite the displacement of the oscillating body.
F = -kx
x
F

## Slide 47: Hooke’s Law
A spring can be stretched or compressed with a force.
The force by which a spring is compressed or stretched is proportional to the magnitude of the displacement (F a x).
Hooke’s Law:
  Felastic = -kx
    Where:
  k = spring constant = stiffness of spring (N/m)
  x = displacement

## Slide 54
Example: A spring is 0.38m long. When it is pulled by a force of 2.0 N, it stretches to 0.42 m. What is the spring constant? Assume the spring behaves elastically.
Extension, ∆x = Stretched length – Original length = . 0.42m – 0.38m = 0.04 m
2.0N = k × 0.04m
So, k = 2.0 N
0.04 m
= 50 N m-1

## Slide 55: Poisson’s ratio Shear stress – strain diagram
Consider a rod of length L, Diameter d and two forces acting at the ends of the Rod as shown in the figure. Then there would be deformation in the length and the diameter of the rod.

## Slide 56
See the Gif image below. The changed Length and diameter would be Δl and Δd respectively.

## Slide 57
Lateral (Transverse )Strain is the ratio of Change in diameter(Δd) to its original diameter(d0).
Then :
In Pull type of load, the diameter goes on decreasing, so it will be negative(-ve).
Linear(Longitudinal) Strain is the ratio of Change in Length(ΔL) to original length (Lo).
In Pull type of load, the length goes on increasing, so it will be positive(+ve).

## Slide 58
Poisson's ratio : is the ratio of lateral strain(transverse contraction) strain to longitudinal extension strain in the direction of stretching force.
Definition of Poisson's ratio
Tensile deformation is considered positive and compressive deformation is considered negative.
The definition of Poisson's ratio contains a minus sign so that normal materials have a positive ratio.
Poisson's ratio, also called Poisson ratio or the Poisson coefficient, or coefficient de Poisson, is usually represented as a lower case Greek nu, .

## Slide 59
Then the Poisson’s ratio define as :
Poisson’s ratio ( ) = -
=
long =
 later(trans) =
 = -

## Slide 60
In tension the long is ( + ) and  is ( - ),but in compression state the long is ( - ) and  is ( + )
For homogeneous ,isotropic solids :
0
A positive (tensile) strain in one direction will also contribute a negative (compressive) strain in the other direction, just as stretching a rubber band to make it longer in one direction makes it thinner in the other directions .

## Slide 61
The Poisson’s ratio is also related to the compressibility of the material. The bulk modulus K or (B) , also called the modulus of compressibility, is the ratio of the hydrostatic pressure p needed for a unit relative decrease in volume ∆V/V:
B(K) =-

## Slide 62
where the minus sign indicates that a compressive pressure (traditionally considered positive) produces a negative volume change. It can be shown that for isotropic materials the bulk modulus is related to the elastic modulus and the Poisson’s ratio as
K =

## Slide 63
Material | Poisson’s Ratio
Cork | 0.5
Rubber | 0.48 to 0.5
Lead | 0.44
Copper | 0.37
Aluminum | 0.35
Stainless Steel | 0.3
Steel | 0.29
Poisson’s ratio for important material

## Slide 64: Example: A cylindrical steel rod with diameter of 0.02m and length of 0.1m(with no force acting on it) it has a load applied in tension of 16KN .Find the change in diameter given a poisson ratio of the material of 0.29 .We previously the deformation portion in the axial direction and got a axial deformation of 2.55x10-5 m (0.0255mm)

## Slide 65
Axial strain =Axial deformation /length
Axial strain =0.0000255/0.1m=0.000255m
long =  later(trans) =
long = later=
 = -
=
=0.29
Diameter1 = 0.02m
Length1=0.1m
d= 0.000001479m
d’=
=0.019998521m